## Slide 1
HUMAN FACTORS ELEMENTS MISSING FROM MOST PSM SYSTEMS
EXAMPLE
HUMAN FACTORS, MANAGEMENT AND ACCIDENTS
OSHA 29 CFR 1910.119 / EPA 40 CFR 68 |  | AIChE/CCPS Risk-Based Process Safety | 
Process Hazard Analysis Operating Procedures Training |  | Process Safety Culture Operating Procedures Operational Readiness | Workforce Involvement Training & Performance Conduct of Operations
PSM systems based on OSHA’s PSM standard likely lack the fundamental human factor standards that if applied across the applicable PSM elements, would work together to reduce human error. The only direct reference to the term “human factors” is mentioned in (e) PHA, which states that the PHA team must consider Human Factors. The Operating Procedures element and Training element are human factors. (f) Operating Procedures states procedures “provide clear instructions for safely conducting activities.” |  | The revised CCPS/AIChE process safety standard Risk Based Process Safety (2007), abandoned the global element on human factors, and instead spread the direct control of Human Factors throughout 6 elements. This change diminished the importance of human factors. The CCPS published the guideline Conduct of Operations and Operational Discipline (2011) to provide further guidance for implementing human factors. Below are summaries of 7 human factors typically missing from PSM systems. | 
FITNESS FOR DUTY
What is it?
Factors that could lead to reduced mental or physical capabilities. Includes: Fatigue, working while sick / stressed / injured, substance abuse.
Why is it important? Weakness in FFD control can lead to 20 times more errors. Working 12 hours shifts for 10 straight days, can increase the error rate for non-routine tasks to 1 mistake in 5 to 10 steps. Fatigue can occur in a broad group of workers at the same time (such as during startup after a maintenance outage/turnaround).
What to do? Develop a Fitness for Duty program to detect and prevent impaired personnel from performing tasks that may affect safety. Includes: Medical evaluations, behavioral observation programs, employee assistance programs, drug and alcohol testing, overtime policies and practices (establish limits for work hours to reduce on-the-job fatigue) and shift scheduling (oversight that minimizes circadian rhythm disruption).
COMMUNICATION
What is it? The exchange of information while preparing for or performing work. Verbal (face-to-face, phone, radio, etc.) and written (email, logs, training material, policies, etc.)
Why is it important? Safety: Helps prevent accidents and ensures that everyone is aware of potential hazards and safety protocols. Efficiency: Streamlines operations, reduces downtime, and ensures that tasks are completed correctly and on time. Problem-Solving: When issues arise, effective communication allows for quick identification and resolution, minimizing disruptions. Team Coordination: Fosters teamwork and ensures that all team members are on the same page, working towards common goals.
What to do? Create a Communication protocol/standard. Including: Repeat back, communicating one task at a time, pre-job meeting, shift turnover, etc.
WORK ENVIRONMENT
What is it? The environment in which the task is performed. Issues include: Temperature extremes, humidity, dust, noise, lighting, working space and housekeeping.
Why is it important? Adverse environment factors can affect other human factors (communication, fatigue, stress), but they also degrade performance independently. Normally affects all humans about the same.
What to do? If possible, plan work in locations to avoid extremes. Otherwise plan for rotations/breaks to minimize effects.
Take into account the increased error rate when using PPE.
Control lighting and minimize communication interference.
TASKS DESIGN AND STAFFING
What is it? Task design: Activities, location, timing, tools, PPE and staff requirements to perform a task successfully. Staffing: Availability of personnel with the proper qualifications for both planned and foreseeable unplanned activities.
Why is it important? A task designed with Human limits is much more likely to work effectively than one that assumes humans can and will “always” do what is written. Task overload (understaffed) and unqualified personnel can increase Human Error up to 10x. Task dependence increases Human Error (The increased probability of failure on subsequent tasks given that an error has already been made).
What to do? Task must consider that humans think, remember and factor in prior data and prior experiences. Includes: Task complexity, error detection/recovery, environment, engineering/administrative controls, etc.
Ensure proper range of expertise and staff size. Including: Emergency/scheduled outages, organizational changes, monitoring rotation, etc.
Error detection and recovery. Including: Error proof mechanisms, automatic alerts, automatic system shutdowns.
Stagger maintenance of redundant equipment. If the same person performs back-to-back maintenance, the probability of making a mistake on Equipment B after making an error on Equipment A, is 1!
HUMAN-SYSTEM INTERFACE AND TOOLS DESIGN
What is it?
Technology through which personnel interact with plant systems to perform their functions and tasks. Includes: Alarms design, workstation layout, error-proofing, control systems integration, labeling, colors, etc.
Why is it important? Operability: Weaknesses in process design can result in increased workload, decreased personnel performance and, an increased likelihood of errors. Maintainability: Weaknesses can result in excessive demands on maintenance personnel, increasing the chance of maintenance errors or problems with equipment reliability and availability. Flexibility: Weaknesses can increase workload and probability of errors.
What to do? Design for operability: Alarm configuration structure to avoid “alarm flooding,” information prioritization (safety systems bypasses, equipment out of service, work in progress, etc.), visual displays (layout, colors), etc.
Design for maintainability: Ensure that personnel are able to perform necessary maintenance activities efficiently.
Design for flexibility: Ensure changes, such as upgrades to the HSI, are planned and put into use.
Full list of Communication rules
PROCEDURES
What is it?
Instructions written with respect to reducing human error that (1) list the steps for a given task and, (2) describe the manner in which the steps are performed.
Why is it important? For procedures to be effective in ensuring tasks are performed correctly, they must be used. Incorrect, incomplete and nonexistent procedures along with action steps difficult to understand/ambiguous and whose information is presented in a confusing manner, all lead to nonuse.
What to do? Create a guideline for developing, writing, formatting and validating procedures that follow best practices for controlling human errors
Create Trouble-Shooting Guides for critical human response
AVAILABLE TIME AND STRESS/STRESSORS
What is it? Available time: Time the task is expected to be required for completion. Work stress: The emotional response that arises when work demands exceed the person’s capacity and capability to cope.
Why is it important? Often the time determined for a task timeframe is calculated using theoretical times where the conditions are “ideal” but not realistic. When task and process duration are not realistic people tend to “find the best and easy way” to get it done. Additionally, in processes where job design, work organization and management systems were not properly considered in design, work stress results. Extreme stress conditions can increase Human Error up to 5x.
What to do? Prevent task overload. Including: Task prioritization/deferral/slippage, delegation, workspace and process design, staffing levels with proper qualifications for both planned and foreseeable unplanned activities.
PSM PROGRAMS COMPARISON
ELEMENTS CONTAINING SOME HUMAN FACTOR STANDARDS
Procedure Writing and Formatting rules
2-20x
HUMAN ERROR
POOR CONTROL OF HUMAN FACTORS
ACCIDENTS
HUMAN ERROR
Natural Hazards
OPERATION AND RISK CONTROL ACTIVITIES
PSM SYSTEMS
HUMANS
Perform
Weak HF Control
Increases HE
Design
99%
1%
Relative impact poor management of each Human Factor has on Human Error Rate