## Slide 1
WILLIAM BRIDGES
wbridges@piii.com
HUMAN RESPONSE IPLs and
HUMAN ERROR PREVENTION IPLs
(beyond administrative controls)
IPL RULES
USING HUMAN AS AN IPL
TYPES OF PROTECTION LAYERS - BEYOND ADMINISTRATIVE CONTROLS
VALIDATION APPROACHES FOR HUMAN IPLs
INDEPENDENT
CAPABLE
MAINTAINED
AUDITED
+
+
+
1. |  | 2. |  | 3. |  | 4. |  | 5.
Determine which parameters limits should have human response, and why human response is best |  | Ensure human response action meets the definition of a Human Response IPL |  | Develop a trouble-shooting guide (general steps for the operators to take) for each response |  | Perform initial training on each human response IPL and do one timed drill of each Human Response IPL per operator per year |  | Validate human response success rates are high enough
SITE SPECIFIC DATA
EXPERT JUDGEMENT
Is there Good to Excellent control of Human Factors?
Consensus of Op. and Maint staff
Is Test/Drill data being collected?
Is site data available for non-drill (actual) responses?
(See Criteria)
Is Expert Judgment allowed by company?
PFD = 1 (No Human IPL)
DT+RT > MART
PFD < 0.1
Round up (order of magnitude)
YES
NO
YES
YES
# | Criteria | True/False
1 | Based on consensus of expert opinion, the operator has less than 15 minutes to successfully detect, diagnose, and perform the required action | 
2 | Operator response is required without explicit criteria and response instructions | 
3 | Critical or emergency responses involve multiple people | 
4 | Response actions provide no feedback that they are effective | 
If all are false, Expert Judgment is allowed
HUMAN ERROR BASELINE Lowest baseline error rate possible: 0.0008
PRACTICE FACTOR
PPY: Number of Practices per year
Use Generic Data + Predicted Data
HUMAN FACTORS MULTIPLIER
Type | Specifics | RRF | Cost ($K)
Bar Code /Scanner | Bar Code – w/o procedure imbedded; combined with interlocks | 3-10 | 0.1
Bar Code /Scanner | Bar Code – with procedure imbedded; combined with interlocks | 3-10 | 0.3
Proof Switches | RFID (radio frequency identification; the reader is hardwired) | 100 | 5
Proof Switches | Proximity Limit Switches (both ends are hardwired) | 10-100 | 0.5
Hardware | Stand-alone valve (spring loaded dead-man valves; for quick draining/venting) | 10-100 | 0.2 to 1
Hardware | Dry disconnects (auto-closing valve on hose end designed to have no leaks on disconnection) | 10-100 | TBD
Hardware | Automated/interlocked valve | 10-100 | 1 to 10
Hardware | Captive Key (value depends on how captive key is administered onsite) | 10-100 | 0.5 to 1
YES
YES
NO
NO
NO
YES
NO
NO
YES
DOWNLOAD
PII FREE RESOURCECS